## Slide 1: CPSC3300: Computer Systems Organization
Lectures 19 & 20 – Cache Performance

## Slide 2: Review: Why Pipeline? For Throughput!
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Inst 0
Inst 1
Inst 2
Inst 4
Inst 3
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
To keep the pipeline running at its maximum rate both I$ and D$ need to satisfy a request from the datapath every cycle.
What happens when they can’t do that?
To avoid a structural hazard need two caches on-chip: one for instructions (I$) and one for data (D$)

## Slide 3: Review: CPU Time
CPI = 1 for pipeline without cache misses

## Slide 4: Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses
CPImemorystall
§5.4 Measuring and Improving Cache Performance
CPI = CPIpipeline + CPImemorystall

## Slide 5: Cache Performance
Definitions:
  CPIpipeline for pipelined processor with ideal cache
    Ideal cache: always cache hit, no cache miss
    focus on CPImemorystall
  Miss rate— misses in the cache divided by the total number of memory accesses to the cache
  Miss penalty — extra cycles to fetch the data to the cache from lower level of the memory hierarchy
Memory-stall clock cycles come primarily from cache misses

## Slide 6: Sample Cache Performance
Chart: Memory Access Time
| 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
4K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
8K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
16K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
32K | 1
64K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 3 | 1 | 1 | 1
128K | 1 | 1 | 1 | 3 | 9 | 7 | 7 | 7 | 7 | 8 | 10 | 25 | 25 | 21 | 2
256K | 1 | 1 | 1 | 3 | 9 | 7 | 7 | 7 | 6 | 12 | 17 | 27 | 26 | 41 | 22 | 2
512K | 1 | 1 | 1 | 3 | 10 | 8 | 8 | 8 | 7 | 13 | 17 | 26 | 25 | 38 | 39 | 21 | 2
1M | 1 | 1 | 2 | 5 | 12 | 13 | 11 | 11 | 11 | 17 | 25 | 26 | 26 | 40 | 41 | 42 | 21 | 1
2M | 1 | 1 | 2 | 5 | 12 | 13 | 11 | 11 | 11 | 17 | 24 | 28 | 29 | 41 | 41 | 39 | 41 | 22 | 2
4M | 1 | 1 | 2 | 5 | 12 | 12 | 11 | 11 | 11 | 14 | 24 | 31 | 30 | 51 | 52 | 47 | 42 | 42 | 21 | 2
8M | 1.6 | 3.5 | 6.4 | 12.1 | 25.4 | 26.6 | 27 | 25 | 24.6 | 25.8 | 38.5 | 60.4 | 47.7 | 56.4 | 55.6 | 57.2 | 55.6 | 45.3 | 46.9 | 23 | 1.7
Data size
L1 miss penalty
Chart: Memory Access Time
| 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
4K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
8K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
16K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
32K | 1
64K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 3 | 1 | 1 | 1
128K | 1 | 1 | 1 | 3 | 9 | 7 | 7 | 7 | 7 | 8 | 10 | 25 | 25 | 21 | 2
256K | 1 | 1 | 1 | 3 | 9 | 7 | 7 | 7 | 6 | 12 | 17 | 27 | 26 | 41 | 22 | 2
512K | 1 | 1 | 1 | 3 | 10 | 8 | 8 | 8 | 7 | 13 | 17 | 26 | 25 | 38 | 39 | 21 | 2
1M | 1 | 1 | 2 | 5 | 12 | 13 | 11 | 11 | 11 | 17 | 25 | 26 | 26 | 40 | 41 | 42 | 21 | 1
2M | 1 | 1 | 2 | 5 | 12 | 13 | 11 | 11 | 11 | 17 | 24 | 28 | 29 | 41 | 41 | 39 | 41 | 22 | 2
4M | 1 | 1 | 2 | 5 | 12 | 12 | 11 | 11 | 11 | 14 | 24 | 31 | 30 | 51 | 52 | 47 | 42 | 42 | 21 | 2
8M | 1.6 | 3.5 | 6.4 | 12.1 | 25.4 | 26.6 | 27 | 25 | 24.6 | 25.8 | 38.5 | 60.4 | 47.7 | 56.4 | 55.6 | 57.2 | 55.6 | 45.3 | 46.9 | 23 | 1.7
L1 miss penalty
L2 miss penalty
L3 miss penalty
L1 hit time
Cache line size

## Slide 7: Homework 6
Measure cache performance on a processor
  Any linux machine in the lab
Note the figure shows
  Y-axis: access time
  X-axis: stride size
  Legend: data size
Identify the machine cache block size as the stride size
  Usually 64 Bytes
  Identify the cache sizes as the legend sizes
    Identify the access time for the stride size at the cache size
    Obtain or calculate the hit time and miss penalty time

## Slide 8: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Every instruction is loaded from I$
  Data load & stores are 36% of instructions
Miss cycles per instruction
  I-cache: 1.0 x 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
Actual CPI = 2 + 2 + 1.44 = 5.44
  Ideal CPU is 5.44/2 =2.72 times faster

## Slide 9: Impacts of Cache Performance
Relative cache penalty increases as processor performance improves (faster clock rate and/or lower CPI)
  The memory speed is unlikely to improve as fast as processor cycle time. When calculating CPIstall, the cache miss penalty is measured in processor clock cycles needed to handle a miss
  The lower the CPIideal, the more pronounced the impact of stalls
  For the example in the previous slide
What if the CPIideal is reduced to 1? 0.5? 0.25?
What if the processor clock rate is doubled (doubling the miss penalty)?
Notes: For ideal CPI = 1, then CPIstall = 4.44 and the amount of execution time spent on memory stalls would have risen from 3.44/5.44 = 63% to 3.44/4.44 = 77%
For miss penalty of 200, memory stall cycles = 2% 200 + 36% x 4% x 200 = 6.88 so that CPIstall = 8.88
This assumes that hit time is not a factor in determining cache performance. A larger cache would have a longer access time (if a lower miss rate), meaning either a slower clock cycle or more stages in the pipeline for memory access.

## Slide 10: Reducing Cache Miss Rates #1
Allow more flexible block placement
In a direct mapped cache a memory block maps to exactly one cache block
At the other extreme, could allow a memory block to be mapped to any cache block – fully associative cache
A compromise is to divide the cache into sets each of which consists of n “ways” (n-way set associative). A memory block maps to a unique set (specified by the index field) and can be placed in any way of that set (so there are n choices)
  (block address) modulo (# sets in the cache)

## Slide 11: Set Associative Cache Example
0
Cache
Main Memory
Q2: How do we find it?
Use next 1 low order memory address bit to determine which cache set (i.e., modulo the number of sets in the cache)
Tag
Data
Q1: Is it there?
Compare all the cache tags in the set to the high order 3 memory address bits to tell if the memory block is in the cache
V
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Two low order bits define the byte in the word (32-b words)
One word blocks
Set
1
0
1
Way
0
1
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block

## Slide 12: A Reference String Mapping
0
4
0
4
Consider the main memory word reference string
  0 4 0 4 0 4 0 4
Start with an empty cache - all blocks initially marked as not valid
Notes: For class handout

## Slide 13: Another Reference String Mapping
0
4
0
4
Consider the main memory word reference string
  0 4 0 4 0 4 0 4
miss
miss
hit
hit
000 Mem(0)
000 Mem(0)
Start with an empty cache - all blocks initially marked as not valid
010 Mem(4)
010 Mem(4)
000 Mem(0)
000 Mem(0)
010 Mem(4)
Solves the ping pong effect in a direct mapped cache due to conflict misses since now two memory locations that map into the same cache set can co-exist!
  8 requests, 2 misses
Notes: For lecture
Another sample string to try 0 1 2 3 0 8 11 0 3

## Slide 14: Four-Way Set Associative Cache
28 = 256 sets each with four ways (each with one block)
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select
Notes: This is called a 4-way set associative cache because there are four cache entries for each cache index. Essentially, you have four direct mapped cache working in parallel.
This is how it works: the cache index selects a set from the cache. The four tags in the set are compared in parallel with the upper bits of the memory address.
If no tags match the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data from the way where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 15: Range of Set Associative Caches
For a fixed size cache, each increase by a factor of two in associativity doubles the number of blocks per set (i.e., the number or ways) and halves the number of sets – decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Block offset
Byte offset
Index
Tag
Notes: For class handout

## Slide 16: Range of Set Associative Caches
For a fixed size cache, each increase by a factor of two in associativity doubles the number of blocks per set (i.e., the number or ways) and halves the number of sets – decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Block offset
Byte offset
Index
Tag
Decreasing associativity
Fully associative
(only one set)
Tag is all the bits except
block and byte offset
Direct mapped
(only one way)
Smaller tags
Increasing associativity
Selects the set
Used for tag compare
Selects the word in the block
Notes: For lecture

## Slide 17: Costs of Set Associative Caches
When a miss occurs, which way’s block do we pick for replacement?
  Least Recently Used (LRU): the block replaced is the one that has been unused for the longest time
    Must have hardware to keep track of when each way’s block was used relative to the other blocks in the set
    For 2-way set associative, takes one bit per set → set the bit when a block is referenced (and reset the other way’s bit)
N-way set associative cache costs
  N comparators (delay and area)
  MUX delay (set selection) before data is available
  Data available after set selection (and Hit/Miss decision). In a direct mapped cache, the cache block is available before the Hit/Miss decision
    So its not possible to just assume a hit and continue and recover later if it was a miss
Notes: First of all, a N-way set associative cache will need N comparators instead of just one comparator (use the right side of the diagram for direct mapped cache).
A N-way set associative cache will also be slower than a direct mapped cache because of this extra multiplexer delay.
Finally, for a N-way set associative cache, the data will be available AFTER the hit/miss signal becomes valid because the hit/mis is needed to control the data MUX.
For a direct mapped cache, that is everything before the MUX on the right or left side, the cache block will be available BEFORE the hit/miss signal (AND gate output) because the data does not have to go through the comparator.
This can be an important consideration because the processor can now go ahead and use the data without knowing if it is a Hit or Miss. Just assume it is a hit.
Since cache hit rate is in the upper 90% range, you will be ahead of the game 90% of the time and for those 10% of the time that you are wrong, just make sure you can recover.
You cannot play this speculation game with a N-way set-associative cache because as I said earlier, the data will not be available to you until the hit/miss signal is valid.
+2 = 38 min. (Y:18)

## Slide 18: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 19: Reducing Cache Miss Rates #2
Use multiple levels of caches
With advancing technology
  bigger L1 caches or
  a unified L2 cache (i.e., it holds both instructions and data) and in some cases even a unified L3 cache
For our example, CPIideal of 2, 100 cycle miss penalty (to main memory), 36% load/stores, a 2% (4%) L1I$ (D$) miss rate, add a UL2$ that has a 25 cycle miss penalty and a 0.5% miss rate
  CPIstalls = 2 + .02×25 + .36×.04×25 + .005×100 + .36×.005×100 = 3.54 (as compared to 5.44 with no L2$)
Notes: Also reduces cache miss penalty

## Slide 20: Multilevel Cache Design Considerations
Design considerations for L1 and L2 caches are different
  L1 cache should focus on minimizing hit time in support of a shorter clock cycle
    Smaller with smaller block sizes
  L2 cache(s) should focus on reducing miss rate to reduce the penalty of long main memory access times
    Larger with larger block sizes
The miss penalty of the L1 cache is significantly reduced by the presence of an L2 cache – so it can be smaller (i.e., faster) but have a higher miss rate
For the L2 cache, hit time is less important than miss rate
  The L2$ hit time determines L1$’s miss penalty
  L2$ local miss rate >> the global miss rate
Notes: Global miss rate – the fraction of references that miss in all levels of a multilevel cache. The global miss rate dictates how often we must access the main memory.
Local miss rate – the fraction of references to one level of a cache that miss

## Slide 21: Key Cache Design Parameters
 | L1 typical | L2 typical
Total size (blocks) | 250 to 2000 | 4000 to 250,000
Total size (KB) | 16 to 64 | 500 to 8000
Block size (B) | 32 to 64 | 32 to 128
Miss penalty (clocks) | 10 to 25 | 100 to 1000
Miss rates (global for L2) | 2% to 5% | 0.1% to 2%

## Slide 22: Two Machines’ Cache Parameters
 | Intel P4 | AMD Opteron
L1 organization | Split I$ and D$ | Split I$ and D$
L1 cache size | 8KB for D$, 96KB for trace cache (~I$) | 64KB for each of I$ and D$
L1 block size | 64 bytes | 64 bytes
L1 associativity | 4-way set assoc. | 2-way set assoc.
L1 replacement | ~ LRU | LRU
L1 write policy | write-through | write-back
L2 organization | Unified | Unified
L2 cache size | 512KB | 1024KB (1MB)
L2 block size | 128 bytes | 64 bytes
L2 associativity | 8-way set assoc. | 16-way set assoc.
L2 replacement | ~LRU | ~LRU
L2 write policy | write-back | write-back
Notes: A trace cache finds a dynamic sequence of instructions including taken branches to load into a cache block. Thus, the cache blocks contain dynamic traces of the executed instructions as determined by the CPU rather than static sequences of instructions as determined by memory layout. It folds branch prediction into the cache.

## Slide 23: 4 Questions for the Memory Hierarchy
Q1: Where can a block be placed in the upper level? (Block placement)
Q2: How is a block found if it is in the upper level? (Block identification)
Q3: Which block should be replaced on a miss? (Block replacement)
Q4: What happens on a write? (Write strategy)

## Slide 24: Q1&Q2: Where can a block be placed/found?
 | # of sets | Blocks per set
Direct mapped | # of blocks in cache | 1
Set associative | (# of blocks in cache)/ associativity | Associativity (typically 2 to 16)
Fully associative | 1 | # of blocks in cache
 | Location method | # of comparisons
Direct mapped | Index | 1
Set associative | Index the set; compare set’s tags | Degree of associativity
Fully associative | Compare all blocks tags | # of blocks

## Slide 25: Q3: Which block should be replaced on a miss?
Easy for direct mapped – only one choice
Set associative or fully associative
  Random
  LRU (Least Recently Used)
For a 2-way set associative cache, random replacement has a miss rate about 1.1 times higher than LRU.
LRU is too costly to implement for high levels of associativity (> 4-way) since tracking the usage information is costly

## Slide 26: Q4: What happens on a write?
Write-through – The information is written to both the block in the cache and to the block in the next lower level of the memory hierarchy
  Write-through is always combined with a write buffer so write waits to lower level memory can be eliminated (as long as the write buffer doesn’t fill)
Write-back – The information is written only to the block in the cache. The modified cache block is written to main memory only when it is replaced.
  Need a dirty bit to keep track of whether the block is clean or dirty
Pros and cons of each?
  Write-through: read misses don’t result in writes (so are simpler and cheaper)
  Write-back: repeated writes require only one write to lower level

## Slide 27: Improving Cache Performance
0. Reduce the time to hit in the cache
  smaller cache
  direct mapped cache
  smaller blocks
  for writes
    no write allocate – no “hit” on cache, just write to write buffer
    write allocate – to avoid two cycles (first check for hit, then write) pipeline writes via a delayed write buffer to cache
1. Reduce the miss rate
  bigger cache
  more flexible placement (increase associativity)
  larger blocks (16 to 64 bytes typical)
  victim cache – small buffer holding most recently discarded blocks

## Slide 28: Improving Cache Performance
2. Reduce the miss penalty
  smaller blocks
  use a write buffer to hold dirty blocks being replaced so don’t have to wait for the write to complete before reading
  check write buffer (and/or victim cache) on read miss – may get lucky
  for large blocks fetch critical word first
  use multiple cache levels – L2 cache not tied to CPU clock rate
  faster backing store/improved memory bandwidth
    wider buses
    memory interleaving, page mode DRAMs

## Slide 29: Summary: The Cache Design Space
Several interacting dimensions
  cache size
  block size
  associativity
  replacement policy
  write-through vs write-back
  write allocation
The optimal choice is a compromise
  depends on access characteristics
    workload
    use (I-cache, D-cache, TLB)
  depends on technology / cost
Simplicity often wins
Associativity
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.