## Slide 1: CPSC3300: Computer Systems Organization
Lectures 17 & 18 – Memory Overview

## Slide 2: Von-Neumann Architecture and Components
We are finished with processor: control and datapath
Move to memory
  How did we use memory in the datapath?
  How many cycles does it take for the mem stage?
Processor
(active)
Computer
Control
(“brain”)
Datapath
(“brawn”)
Memory
(passive)
(where
programs,
data
live when
running)
Devices
Input
Output
Keyboard, Mouse
Display, Printer
Disk (where
programs,
data
live when
not running)

## Slide 3: The Processor-DRAM Performance Gap
Typical CPU clock rate
  1-4 GHz (< 1ns cycle time)
Typical DRAM access time
  30 ns (> 30 cycles)
Typical main memory access
200ns (DRAM access time, precharge, chip crossing, overhead)
Our pipeline designs assume 1 cycle access
The problem gets worse: CPUs faster, memories bigger (slow)
Solution: big memories are slow, small memories can be made fast

## Slide 4: Eight Great Ideas
Design for Moore’s Law
Use abstraction to simplify design
Make the common case fast
Performance via parallelism
Performance via pipelining
Performance via prediction
Hierarchy of memories
Dependability via redundancy

## Slide 5: Principle of Locality
Programs access a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, induction variables
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data

## Slide 6: Memory Hierarchy Pyramid
Processor (CPU)
Size of memory at each level
Level 1
Level 2
Level n
Increasing Distance from CPU, Decreasing cost / MB
Level 3
. . .
transfer datapath: bus
Decreasing distance
from CPU, Decreasing Access Time (Memory Latency)

## Slide 7: Memory
a memory – a logical k × m array of stored bits.
•
•
•
k = 2n
locations
m bits
Address Space:
number of locations (usually a power of 2)
Addressability:
number of bits per location (e.g., byte-addressable)

## Slide 8: Memory Organization Example
Example memory contents:
  A memory with 3 address bits & 8 data bits has:
  k = 3 and n = 8 so 23 = 8 addresses labeled 0 to 7.
  23 = 8 words of 8-bit data
Memory Address
Binary Decimal
Memory
Content
0 0 0 0
1 0 0 0 1 1 1 1
0 0 1 1
1 1 1 1 1 1 1 1
0 1 0 2
1 0 1 1 0 0 0 1
0 1 1 3
0 0 0 0 0 0 0 0
1 0 0 4
1 0 1 1 1 0 0 1
1 0 1 5
1 0 0 0 0 1 1 0
1
1 0 6
0 0 1 1 0 0 1 1
1 1 1 7
1 1 0 0 1 1 0 0

## Slide 9: Basic Memory Operations
Memory operations 3-tuple:
  Data ─ written to or read from memory
  Address ─ specifies memory location
  Command ─ READ or WRITE

## Slide 10: RAM Integrated Circuits
Types of random access memory
  Static – information stored in latches
  Dynamic – information stored as electrical charges on capacitors
    Charge “leaks” off
    Periodic refresh of charge required
Dependence on Power Supply
  Volatile – loses stored information when power turned off
  Non-volatile – retains information when power turned off

## Slide 11: Memory Technology
Static RAM (SRAM)
  0.5ns – 2.5ns, $500 – $1,000 per GB
Dynamic RAM (DRAM)
  50ns – 70ns, $3 – $10 per GB
Flash Memory
  0.005ms – 0.05ms, $0.25 - $0.75 per GB
Magnetic disk
  5ms – 20ms, $0.02 – $0.05 per GB
Ideal memory
  Access time of SRAM
  Capacity and cost/GB of disk

## Slide 12: SRAM
Array of storage cells used to implement static RAM
Storage Cell
  SR Latch
  Select input for control
  Dual Rail Data Inputs B and B
  Dual Rail Data Outputs C and C
Select
B
RAM cell
C
C
B
S
R
Q
Q

## Slide 13: Dynamic RAM (DRAM)
Basic Principle: Storage of information on capacitors.
Charge and discharge of capacitor to change stored value
Use of transistor as “switch” to:
  Store charge
  Charge or discharge

## Slide 14: Dynamic RAM (continued)
(a)
(c)
Select
D
C
Q
B
DRAM cell
model
C
(f)
(g)
(h)
Select
B
T
C
DRAM cell
To Pump
(b)
(d)
(e)
Stored 1
Stored 0
Write 1
Write 0
Read 1
Read 0
Notes: Warning: (d), (e), (f), and (g) are animated. Each animation is triggered with a mouse click
and goes through two steps at 1 second intervals.

## Slide 15: Current Memory Hierarchy
Control
Data- path
Processor
regs
Secon-
dary
Mem-
ory
L2
Cache
Speed(ns): 0.5ns 1.5ns 5ns 50ns 10,000,000ns Size (MB): 0.0005 0.1 1-4 128-32,768 1,000,000 Cost ($/GB): -- $1,500 $500 $5 < $0.05 Technology: Regs SRAM SRAM DRAM Disk
L1 cache
Main
Mem-
ory
L3
Cache
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality.
+1 = 7 min. (X:47)

## Slide 16: Disk Storage
Nonvolatile, rotating magnetic storage

## Slide 17: Disk Sectors and Access
Each sector records
  Sector ID
  Data (512 bytes, 4096 bytes (Advanced Format))
  Error correcting code (ECC)
    Used to hide defects and recording errors
  Synchronization fields and gaps
Access to a sector involves
  Queuing delay if other accesses are pending
  Seek: move the heads
  Rotational latency
  Data transfer
  Controller overhead

## Slide 18: Disk Access Example
Given
  512B sector, 15,000rpm, 4ms average seek time, 100MB/s transfer rate, 0.2ms controller overhead, idle disk
Average read time
  4ms seek time + ½ / (15,000/60) = 2ms rotational latency + 512 / 100MB/s = 0.005ms transfer time + 0.2ms controller delay = 6.2ms
If actual average seek time is 1ms
  Average read time = 3.2ms

## Slide 19: Taking Advantage of Locality
Memory hierarchy
Store everything on disk
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory attached to CPU

## Slide 20: Memory Hierarchy Levels
Block (aka line): unit of copying
  May be multiple words
If accessed data is present in upper level
  Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio
  Then accessed data supplied from upper level

## Slide 21: Sample Cache Performance
Chart: Memory Access Time
| 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
4K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
8K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
16K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
32K | 1
64K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 3 | 1 | 1 | 1
128K | 1 | 1 | 1 | 3 | 9 | 7 | 7 | 7 | 7 | 8 | 10 | 25 | 25 | 21 | 2
256K | 1 | 1 | 1 | 3 | 9 | 7 | 7 | 7 | 6 | 12 | 17 | 27 | 26 | 41 | 22 | 2
512K | 1 | 1 | 1 | 3 | 10 | 8 | 8 | 8 | 7 | 13 | 17 | 26 | 25 | 38 | 39 | 21 | 2
1M | 1 | 1 | 2 | 5 | 12 | 13 | 11 | 11 | 11 | 17 | 25 | 26 | 26 | 40 | 41 | 42 | 21 | 1
2M | 1 | 1 | 2 | 5 | 12 | 13 | 11 | 11 | 11 | 17 | 24 | 28 | 29 | 41 | 41 | 39 | 41 | 22 | 2
4M | 1 | 1 | 2 | 5 | 12 | 12 | 11 | 11 | 11 | 14 | 24 | 31 | 30 | 51 | 52 | 47 | 42 | 42 | 21 | 2
8M | 1.6 | 3.5 | 6.4 | 12.1 | 25.4 | 26.6 | 27 | 25 | 24.6 | 25.8 | 38.5 | 60.4 | 47.7 | 56.4 | 55.6 | 57.2 | 55.6 | 45.3 | 46.9 | 23 | 1.7
Data size
L1 miss penalty
Chart: Memory Access Time
| 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
4K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
8K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
16K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
32K | 1
64K | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 3 | 1 | 1 | 1
128K | 1 | 1 | 1 | 3 | 9 | 7 | 7 | 7 | 7 | 8 | 10 | 25 | 25 | 21 | 2
256K | 1 | 1 | 1 | 3 | 9 | 7 | 7 | 7 | 6 | 12 | 17 | 27 | 26 | 41 | 22 | 2
512K | 1 | 1 | 1 | 3 | 10 | 8 | 8 | 8 | 7 | 13 | 17 | 26 | 25 | 38 | 39 | 21 | 2
1M | 1 | 1 | 2 | 5 | 12 | 13 | 11 | 11 | 11 | 17 | 25 | 26 | 26 | 40 | 41 | 42 | 21 | 1
2M | 1 | 1 | 2 | 5 | 12 | 13 | 11 | 11 | 11 | 17 | 24 | 28 | 29 | 41 | 41 | 39 | 41 | 22 | 2
4M | 1 | 1 | 2 | 5 | 12 | 12 | 11 | 11 | 11 | 14 | 24 | 31 | 30 | 51 | 52 | 47 | 42 | 42 | 21 | 2
8M | 1.6 | 3.5 | 6.4 | 12.1 | 25.4 | 26.6 | 27 | 25 | 24.6 | 25.8 | 38.5 | 60.4 | 47.7 | 56.4 | 55.6 | 57.2 | 55.6 | 45.3 | 46.9 | 23 | 1.7
L1 miss penalty
L2 miss penalty
L3 miss penalty
L1 hit time

## Slide 22: Administrivia
Exam II
  Tuesday, April 3
  Covering materials up through lecture 16 (Real Processor Design Examples), end of chapter 4 (after exam I)
Study guide (exam II review / outline of topics) and a sample exam will be available on canvas
Homework solutions will be made available on canvas

## Slide 23: Cache Memory
Cache memory
  The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
§5.3 The Basics of Caches
How do we know if the data is present?
Where do we look?

## Slide 24: Direct Mapped Cache
Location determined by address
Direct mapped: only one choice
  (Block address) modulo (#Blocks in cache)
#Blocks is a power of 2
  8 in the example
Use low-order address bits
  Multiple blocks in lower level map to the same cache location
  4  1 in the example

## Slide 25: Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 26: Cache Example
8-blocks, 1 word/block, direct mapped
  1 word = 4 bytes
Initial state
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 27: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 28: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 

## Slide 29: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 30: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 31: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 32: Address Subdivision
2^10 entries in the cache
Each entry: 20-bit tag, 32-bit (4 bytes) data, 1-bit valid

## Slide 33: Example: Larger Block Size
Given a 32-bit machine
64 blocks in the direct mapped cache, 16 bytes/block
  To what block number does address 1200 map?
  To answer this question, how many bits for tag, index, and offset?
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits
(1200)10 = (01 001011 0000)2
tag index offset
        01 11 0

## Slide 34: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer of them
    More competition  increased miss rate
  Larger blocks  pollution
Larger miss penalty
  Can override benefit of reduced miss rate
  Early restart and critical-word-first can help

## Slide 35: Reducing Cache Misses
Instructions
  Reorder procedures in memory so as to reduce misses
  Profiling to look at conflicts
  McFarling [1989] reduced caches misses by 75% on 8KB direct mapped cache with 4 byte blocks
Data
  Increase temporal and spatial locality in algorithms

## Slide 36: Summary
Locality
  Temporal locality and spatial locality
Memory hierarchy
Direct mapped cache